## Slide 1: HABs: A Cost Perspective
Caleb Owen
City of Thornton
SPCURE: Confluence at the Confluence
12/14/21

## Slide 2: Overview
Thornton Overview
Monitoring Costs
Source Treatment Costs
WTP Chemical Costs
Capital Project Costs

## Slide 3: Raw Water Supply
Upper Clear Creek
  12K acft storage in Standley Lake
  High quality source
Lower Clear Creek
  2K acft storage in West Gravel Lake System
  Okay quality source
South Platte River
  21.2K acft in East Gravel Lake System
  Challenging quality source
Chart: Source Water Averages
| 2018 | 2019 | 2020 | 2021
South Platte | 4.94 | 3.25 | 4.24 | 3.05
Lower Clear Creek | 1.12 | 0.95 | 1.01 | 0.84
Upper Clear Creek | 0.05 | 0.09 | 0.1 | 0.19
Chart: o-Phosphate (ppm)
| 2018 | 2019 | 2020 | 2021
South Platte | 2.02 | 1.4 | 1.44 | 1.4
Lower Clear Creek | 0.59 | 0.65 | 1.27 | 1.35
Upper Clear Creek | 0.05 | 0.07 | 0.05 | 0.07

## Slide 4: City of Thornton
~150,000 customers
38 MGD avg. summer consumption
Top customer complaint: T&O
Two WTPs
  Wes Brown WTP - 50 MGD
    Ultrafiltration Membranes
    Treats SP & LCC
    Retrofit 2005
  Thornton WTP – 20 MGD
    Advanced Oxidation and Biofiltration
    Treats SP & UCC
    Built 2020
    ~$100M

## Slide 5: HABs Strategy
Monitoring
  Visual Inspection
  Lab –T&O, Algae, Chl-a, Toxins
Raw Water Treatment
  Algaecide
  SolarBees
  Natural Attenuation
Water Treatment
  Blending
  Biofiltration
  PAC
Wait it out until winter 

## Slide 6: Visual Inspections
2-3 Inspections/wk
  Very Important!
  Try to catch blooms early

## Slide 7: Toxin and T&O Monitoring
Weekly Abraxis Test Strips
  3 lakes/wk
  $3000/yr
LC-MS/MS Toxin Testing
  2-3 lakes/qtr
  $3000/yr
  Confirmation testing req. for positive Abraxis tests
GC-MS T&O testing
  11-19 samples/wk
  $116,000 purchase price + $12K/yr service

## Slide 8: T&O - PACulator

## Slide 9: Algae & Chl-a Monitoring
Weekly monitoring
  8 lakes/wk
  1 staff, 2-3 hrs/wk
  Helps guide algaecide application
Dominant Summer Species
  SP: Anabaena, Microcystis, Oscillatoria, Aphanizomenon
  LCC: More Chlorophytes + Anabaena, Microcystis, Oscillatoria
  UCC: Diatoms

## Slide 10: Algaecide
CuSO4
  $25,000/yr
  Reqs. pontoon boat
  2-3 staff member crew
  Treat 2-3 lakes/day
  4-5 treatments/lake/summer
  Targeted applications

## Slide 12: Raw Water Treatment
Solar Bees
  3-8/lake in 3 lakes
  $450K purchase + $36K/yr service
  Cleaned monthly
    2 person crew
    Full day effort

## Slide 14: Chemical Costs
Wes Brown WTP
  $0.33 - 0.51/Kgal
  Avg. PAC $500K/yr
    10-40 ppm dose
    Up to $15K/day @ max flow & dose
Thornton WTP
  $0.20 - 0.35/Kgal
  Even at 100% SP source, cheaper to treat
    Biofiltration > PAC

## Slide 15: Blending
Quantity limited, especially Clear Creek supplies
New plant can treat SP
  >99% T&O removal
Wes Brown Plant
  Adjust according to WQI
  ~90% T&O removal max

## Slide 16: Other Projects
Lakes in Series
  Move water through 7 lakes
  ~$240K annual pumping costs
  Expecting natural attenuation of nutrients
  Too soon to know WQ impact
Hypo Relocation
  $1.8M project, completed 2019
  Avg. saving $500K/yr on PAC and hypo costs

## Slide 17: Summary
Thornton HABs Strategy
  ~$850K/yr
  Excluding employee time
Best bang for your buck
  Getting visual on the lake
  Targeted algaecide, applied early in bloom
  Frequent T&O monitoring to adjust PAC dose
Biggest Costs
  PAC
  Infrastructure
  Personnel, Time, & Expertise

## Slide 18: Questions?