## Slide 1
Instream, Wet-weather Nutrient Trends
Holly Piza, P.E., D. WRE
October 6, 2022

## Slide 2
1998-2018, 20 years of data!
Phase 1 MS4 requirement for instream, wet weather monitoring
JTF = MHFD, Denver, Aurora, and Lakewood
USGS and Colorado DWR streamflow gaging stations
MHFD ALERT rainfall stations
  Stream flow
  Precipitation
Refrigerated autosamplers remotely operated
  24-hour composite water quality sample
Background

## Slide 3
1
Sand
2
3
TG
Notes: 541 composite samples over 20 years of data

## Slide 4
Composite Samples
  Seasonally (Apr-Oct)
  Lab analysis of physicochemical, ions, nutrients, metals, and solids
Trend analysis focused on…
  Conductivity
  Total Suspended Solids
  Total Nitrogen
  Total Phosphorus
Data Collection

## Slide 5
  Stormflow = Discharge – Baseflow
Bounds on Hydrology
Notes:   (SPR) Chatfield Reservoir releases and (Sand) Aurora Water Reuse Facility
Account for changes in baseflow and concentrations

## Slide 6
Total Suspended Solids (TSS) Concentrations
1
2
3
Sand

## Slide 7
Total Phosphorus Concentrations
1
2
3
Sand

## Slide 8
Trend Analysis South Platte River at Denver

## Slide 9
Water Quality Trends
Water Quality | South Platte River below Union Avenue | South Platte River at Denver | Toll Gate Creek above 6th Avenue | Sand Creek above Burlington Ditch | South Platte River at Henderson
Suspended Solids, Total (mg/L) | X | X | X | ▼ | ▼
Specific Conductance (µS/cm) | ▲ | X | ▲ | ▲ | X
Nitrogen, Total (mg/L) | X | X | X | X | ▼
Phosphorus, Total (mg/L) | X | ▼ | X | X | ▼
▼ Significant decreasing trend |  |  |  |  | 
▲ Significant increasing trend |  |  |  |  | 
X No trend |  |  |  |  | 
1
3
2
Sand
TG

## Slide 10
Base Flow Hydrology Trend – SPR Denver (2)
No Trend

## Slide 11
Significant decrease by 6.5 cfs per year
Base Flow Hydrology Trend – Sand Creek

## Slide 12
Loads
Storm Loads Trend Analysis

## Slide 13
Normalized Loads Pounds per day
South Platte River at Denver |  |  |  | 
Analyte | No. Storm Samples | Min. | Max | Mean
Nitrogen, Total | 124 | 951 | 76,565 | 11,074
Phosphorus, Total | 126 | 57 | 13,136 | 1,995
Total Suspended Solids | 128 | 12,233 | 10,984,394 | 1,105,888
South Platte River below Union Avenue |  |  |  | 
Analyte | No. Storms Samples | Minimum | Max | Mean
Nitrogen, Total | 89 | 48 | 10,698 | 1,613
Phosphorus, Total | 93 | 3 | 3,124 | 316
Total Suspended Solids | 93 | 32 | 2,960,239 | 245,761
South Platte River at Henderson |  |  |  | 
Analyte | No. Storms Samples | Min. | Max | Mean
Nitrogen, Total | 91 | 1,826 | 103,730 | 23,253
Phosphorus, Total | 95 | 282 | 23,398 | 4,709
Total Suspended Solids | 97 | 7,530 | 19,761,101 | 2,040,847
Sand Creek above Burlington Ditch |  |  |  | 
Analyte | No. Storms Samples | Min. | Max | Mean
Nitrogen, Total | 88 | 169 | 38,388 | 4,221
Phosphorus, Total | 92 | 28 | 14,862 | 1,198
Total Suspended Solids | 94 | 2,536 | 10,568,654 | 834,797

## Slide 14
Total Suspended Solids Loads
1
2
3
Sand

## Slide 15
Total Phosphorus Loads
1
2
3
Sand

## Slide 16
Trend Analysis Summary
Water Quality | South Platte River below Union Avenue | South Platte River at Denver | Toll Gate Creek above 6th Avenue | Sand Creek above Burlington Ditch | South Platte River at Henderson
Suspended Solids, Total (mg/L) | X | X | X | ▼ | ▼
Specific Conductance (µS/cm) | ▲ | X | ▲ | ▲ | X
Nitrogen, Total (mg/L) | X | X | X | X | ▼
Phosphorus, Total (mg/L) | X | ▼ | X | X | ▼
Discharge |  | South Platte River at Denver | Sand Creek above Burlington Ditch | Sand Creek above Burlington Ditch | South Platte River at Henderson
Discharge (cfs) | X | X | X | ▼ | X
Loads |  | South Platte River at Denver | Sand Creek above Burlington Ditch | Sand Creek above Burlington Ditch | South Platte River at Henderson
Suspended Solids, Total (#/day) | X | X | X | ▼ | X
Nitrogen, Total (#/day) | X | X | X | X | X
Phosphorus, Total (#/day) | X | X | X | ▼ | X
▼ Significant decreasing trend |  |  |  |  | 
▲ Significant increasing trend |  |  |  |  | 
X No trend |  |  |  |  | 
1
3
2
Sand
TG

## Slide 17
Thank You!